## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 9: Truth Tables and Karnaugh Maps

## Slide 2: Truth Table from SOP
A’BC + ABC + ABC’ + A’BC’ = 0’11 + 111 + 110’ + 0’10’
The only truth table lines that give 1
A | B | C | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 3: Truth Table from POS
(A’ + B + C) (A + B + C)(A + B + C’)(A’ + B + C’) = (1’+0+0)(0+0+0)(0+0+1’)(1’+0+1’)
The only truth table lines that give 0
A | B | C | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 4: Converting Standard Form to the Other
Convert the one you have to a truth table
Find the opposite logic terms
Write the terms out

## Slide 5: Example
(A + B + C’)(A’ + B’ + C’)(A + B’ + C)
A’B’C’ + A’BC + AB’C’ + AB’C + ABC’
A | B | C | Output
0 | 0 | 0 | 
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 0

## Slide 6: Example
ABC’ + A’B’C’ + AB’C
(A+B+C’)(A+B’+C)(A+B’+C’)(A’+B+C)(A’+B’+C’)
A | B | C | Output
0 | 0 | 0 | 1
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 

## Slide 7: Simplification
Boolean Algebra
Karnaugh Maps

## Slide 8: Karnaugh Map
Visual way to reduce logic statements to the simplest forms
Good for 4-5 inputs

## Slide 9: Truth Table to Karnaugh Map
A | B | C | D | Output
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
A | B | C | D | Output
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0

## Slide 10: Karnaugh Map of Standard SOP
A standard SOP gives all terms that have output of 1
Same as converting a truth table

## Slide 11: Karnaugh Map of Non-Standard SOP
Terms need to be expanded to include all input options
B’ + A’B + ABC’
Then put into the map
B’ | A’B | ABC’
000 | 010 | 110
001 | 011 | 
100 |  | 
101 |  | 
1
1
1
1
1
1
1
0

## Slide 12: SOP Minimization
Make groups of 1’s (by a power of 2)
  1’s that are adjacent
  Groups that are squares or rectangles only
  Make the biggest ones possible
  Overlap is okay
  Complete overlaps are not used

## Slide 13: Examples

## Slide 14: SOP Minimization
Next make a minimum product term for the group
3 Input Variables | 
1 cell | 3 input product term
2 cells | 2 input product term
4 cells | 1 input product term
8 cells | All terms true, F=1
4 Input Variables | 
1 cell | 4 input product term
2 cells | 3 input product term
4 cells | 2 input product term
8 cells | 1 input product term
16 cells | All terms true, F=1

## Slide 15: Example
B’ + A’B + ABC’
3 4-cell groups
A’ + B’ + C’
1
1
1
1
1
1
1
0

## Slide 16: Examples

## Slide 17: Examples
Minimize:
AB + AC’ + A’BC
ABC’ + BC’ + D

## Slide 18: Don’t Care Condition
Used for conditions that cannot occur
Can be used to further simplify logic

## Slide 19: Example
Can be used to further simplify logic
1
1
1
1
1
X
X

## Slide 20: Reading
This lecture
  Sections 4.7-4.9
Next lecture
  Sections 1.8, 3.9, 4.10-4.11, Ch4 Applied Logic