## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 15: Comparators and Decoders/Encoders

## Slide 2: Comparator
End Goal:
  4-bit input numbers
  <, >, = outputs

## Slide 3: Starting Small
1-bit
  A<B
  A=B
  A>B

## Slide 4: Equality
XNOR (A B)

## Slide 5: Truth Table
A<B = A’B
A=B = A’B’ + AB = A B
A>B = AB’
A | B | A<B | A=B | A>B
0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0

## Slide 6: Circuit
A<B = A’B
A=B = A B
A>B = AB’

## Slide 7: 2-bit Comparator
Same process
A1 | A0 | B1 | B0 | A<B | A=B | A>B
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0
A1 | A0 | B1 | B0 | A<B | A=B | A>B
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0

## Slide 8: Karnaugh Maps

## Slide 9: Boolean Expressions
A>B: A1B1’ + A0B1’B0’ + A1A0B0’
A=B: A1’A0’B1’B0’ + A1’A0B1’B0 +
A1A0B1B0 + A1A0’B1B0’
: A1’B1’ (A0’B0’ + A0B0) + A1B1 (A0B0 + A0’B0’)
: (A0B0 + A0’B0’) (A1B1 + A1’B1’)
: (A0 B0) (A1 B1)
A<B: A1’B1 + A0’B1B0 + A1’A0’B0

## Slide 10: Circuit

## Slide 11: Generalize
A>B
  If A1 = 1 and B1 = 0
  If A1 = B1 and A0 = 1 and B0 = 0
    A1=B1 means when they are both 0 and both 1
A<B
  If A1 = 0 and B1 = 1
  If A1 = B1 and A0 = 0 and B0 = 1
A=B
  (A1 B1) (A0 B0)

## Slide 12: 4-bit Comparator
Use generalized rules
  8-bits is too many inputs for a Karnaugh map
  Create a circuit from the rules
A>B
  If A3 = 1 and B3 = 0
  If A3 = B3 and A2 = 1 and B2 = 0
  If A3 = B3, A2 = B2 and A1 = 1 and B1 = 0
  If A3 = B3, A2 = B2, A1 = B1 and A0 = 1 and B0 = 0

## Slide 13: 4-bit Comparator

## Slide 14: Larger Comparators
Input AND output comparator signals to ripple the results
Inputs treated
as 5th bit

## Slide 15: Comparator Applications
Sensors
  Temperature, position compared to a setting
Motor control
  Like in 3-D printers
Password verification

## Slide 16: Decoders
An input combination
activates one output
n inputs, 2^n outputs
  1 to 2, 2 to 4, 3 to 8, 4 to 16

## Slide 17: Active High vs Active Low
Active High = ON means 1
Active Low = ON means 0
This chip is active low

## Slide 18: Active Low Decoder

## Slide 19: Basics
Input = 1001
Active high output
AND

## Slide 20: Basics
Input = 1001
Active low output
NAND
Chip would have
16 of these

## Slide 21: Applications
Memory Addressing
  Turn on a specific bank of memory
Turn specific things on and off
  Ex TV vs projector screen

## Slide 22: Encoders
Reverse of decoder
2^n inputs, n outputs

## Slide 23: Basics
8 to 3 encoder (binary to octal)

## Slide 24: Application
Keypad
Encoded output
is easier to transmit
and use

## Slide 25: Reading
This lecture
  Sections 6.4-6.6
Next lecture
  Sections 6.8-6.10