## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 16: Multiplexers and Parity

## Slide 2: Multiplexer
Usually called a MUX
Has both encoder and decoder inputs
  n selection inputs and 2^n data inputs
  One output
  n selects which of 2^n
  is on the output

## Slide 3: MUX

## Slide 4: MUX

## Slide 5: MUX

## Slide 6: Example

## Slide 7: Example

## Slide 8: Transmission Modes
Simplex Transmission Mode
  Television, radio, above MUX circuit
Half Duplex Transmission Mode
  Walkie-talkie
Full Duplex Transmission Mode
  Phones

## Slide 9: Half Duplex Example
Not really a MUX, but a MUX switch

## Slide 10: Real Chips – 74HC153
Dual 4-input MUX
Now with enable

## Slide 11: Real Chips – 74HC151
8-input MUX

## Slide 12: Demultiplexer (DEMUX)
Reverse of MUX
  n selection inputs and one data input
  2^n data outputs
  n selects pins tell which of 2^n
  the input goes onto

## Slide 13: DEMUX
S1 | S0 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | Input
0 | 1 | 0 | 0 | Input | 0
1 | 0 | 0 | Input | 0 | 0
1 | 1 | Input | 0 | 0 | 0

## Slide 14: Decoder as DEMUX
One CS line becomes
data input
Active low example

## Slide 15: DEMUX Applications
Like a chip select to pick what subsystem
to communicate with
  Computer to projector or monitor
Memory addressing and comms
Serial to parallel conversion

## Slide 16: Parity
A form of error checking
Even parity - # of 1’s in a transmission is even
  Sum of all bits is 0
Odd parity - # of 1’s in a transmission is odd
  Sum of all bits is 1

## Slide 17: Examples
Even or odd parity?
1000 0100
1010 0101
1110 0000
0110 0100
0110 1010

## Slide 18: Parity for Error Checking
One less data bit than packet size
  Replaced with parity bit
  Packets without parity are discarded
    Packet can be any size
    Larger packets should have more robust error checking

## Slide 19: Communication w/Parity
One form of parity must be chosen
Generate parity bits to ensure the chosen form
Parity check passes if received data has the chosen form, otherwise error occurred

## Slide 20: Examples
Assume even parity communication
  Find the parity bit x
1000 010x
1010 010x
1110 000x
0110 010x
0110 101x

## Slide 21: Examples
Assume even parity communication
  Is there a packet error?
1000 0101
1010 0100
1110 0001
0110 0101
0110 1011

## Slide 22: Generating Parity
Sum all bits to get even parity bit
Sum and NOT to get odd parity

## Slide 23: Checking Parity
Same as generating, but with an extra bit
  Use opposite parity to indicate an error

## Slide 24: Real Chips – 74HC280
9-bit parity generator/checker

## Slide 25: Use

## Slide 26: Reading
This lecture
  Sections 6.8-6.10
Next lecture
  Sections 5.7, 6.11, 7.1