## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 21: Shift Registers

## Slide 2: Outline
Flip-Flop Review
Shift Register Intro
5 Types of shift register configurations
Notes on real chips

## Slide 3: Flip-Flop Applications
Data Storage
  Ch8
Frequency Division
Counting
  Ch9

## Slide 4: D Flip-Flop

## Slide 5: Shift Registers
No set state machine
Shift data in from external sources
A series of flip-flops

## Slide 6: Register
A digital circuit with 2 functions
  Data storage

## Slide 7: Register
  Data movement (4-bit examples)

## Slide 8: Serial vs. Parallel
Serial is one line
  Connection count is small and takes little space
  Used in long distance comms
Parallel is one line per bit
  Very fast because all bits are xferred at once
  Takes up much more space than serial
  Used in short distance comms (moving variables)

## Slide 9: Serial in / Serial out (SISO)
Like a queue or buffer
  Buffering in a long xfer line
Destructive readout (all these regs do this)

## Slide 10: SISO Circuit
Simplest version

## Slide 11: SISO Data Table Example

## Slide 12: SISO Signal Example

## Slide 13: Serial in / Parallel out (SIPO)
Converts data format
Receives data from serial bus and stores into variable

## Slide 14: SIPO Circuit
Read all outputs at any time

## Slide 15: SIPO Signal Example

## Slide 16: Parallel in / Serial out (PISO)
Converts data format
Gets data ready to be xferred on serial bus

## Slide 17: PISO Circuit

## Slide 18: PISO Signal Example
|| data is 0101

## Slide 19: Parallel in / Parallel out (PIPO)
Move variables around
  Between registers
  Into/out of memory

## Slide 20: PIPO Circuit

## Slide 21: PIPO Signal Example

## Slide 22: Bit Rotation
Usually bidirectional (data can go both directions)
  Using direction input line

## Slide 23: Bit Rotation
Shift 0100 to the left, get 1000 (0100 << 1)
  What is that equivalent to?
Shift 0100 to the right, get 0010 (0100 >> 1)
  What is that equivalent to?
What is 5<<1? 7>>1? 9>>2? 1<<4? 3>>3?

## Slide 24: Signal Example

## Slide 25: Circuit

## Slide 26: Real Chips
The real chips have additional functionality
  PIPO and SIPO in one chip
  SISO and PISO in one chip
  SISO, SIPO, PISO, and PIPO in one chip
    Universal shift register

## Slide 27: Reading
This lecture
  Sections 8.1-8.3
Next lecture
  Sections 8.4-8.7