## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 22: Shift Registers 2

## Slide 2: Outline
Shift Register Counters
  Johnson Counter
  Ring Counter
Shift Register Applications
Troubleshooting

## Slide 3: Shift Register Counter
Output is connected back to input
  Are also considered counters (Ch9)
Have a specified sequence of states

## Slide 4: Johnson Counter
Creates a clock frequency that is 2n slower that CLK
  n is the number of bits in the counter
Ex: if CLK is 1MHz and the counter has 5 bits
  Johnson counter freq = 1MHZ/(2*5) = 100kHz

## Slide 5: Circuit

## Slide 6: Signal Example
Measure output in
one spot
No signal
setup required

## Slide 7: Ring Counter
Like a Johnson counter, but with any bit pattern
The pattern continuously goes through all flip-flops and then back to the beginning

## Slide 8: Circuit
No use of Q’
Use Preset to insert bit sequence

## Slide 9: Logic Table
Read any flip-flop output to watch the sequence

## Slide 10: Signal Example
Needs PRE’
on CLK 1 & 3
to set the seq
  You set that up
  externally

## Slide 11: Applications
Time Delay
Serial to Parallel Converter
UART Transmitter
Keyboard Encoder

## Slide 12: Time Delay
Insert a delay into some signals
  Allow for setup time on a part w/o delaying a uC

## Slide 13: Another Option

## Slide 14: Serial to Parallel Converter
Serial is one line
  Connection count is small and takes little space
Parallel is one line per bit
  Very fast because all bits are xferred at once
  Takes up much more space than serial

## Slide 15: Serial to Parallel Converter

## Slide 16: UART
Universal Asynchronous Receiver Transmitter
  Full Duplex (RX and TX as same time)
  Asynchronous (no clock)
  Serial data xfer
  Low overhead

## Slide 17: UART
PISO transmit / SIPO receive

## Slide 18: Keyboard Encoder
Get key press data to send over USB to computer
  Simplified with no key press memory buffer
Scans for pressed keys
Encodes key presses and stores for TX
Debounces a key press

## Slide 20: Real Chip – 74HC194
Universal shift reg

## Slide 21: Exercising a Circuit
Put all parts of the circuit through all possible states
  Tests all chips for working status
  Tests all circuit connections
  More complicated with more memory parts or complexity

## Slide 22: Example (SIPO Test)
Using circuit from Serial to Parallel Converter earlier

## Slide 23: Reading
This lecture
  Sections 8.4-8.7
Next lecture
  9.1-9.4