## Slide 1: CPE201 Digital Design
By Benjamin Haas
Class 27: Transmission and Buses

## Slide 2: Outline
Bus Parameters
Parallel Buses
Serial Buses

## Slide 3: Buses
We are dealing with layer 1 and 2
  1 is bus type (Bluetooth, SPI, RS232, USB, etc.)
  2 is 802 standards (802.11 wifi, 802.3 eth, etc.)

## Slide 4: Bus Parameters
Things You’ve Seen
  Serial/Parallel
    1 bit at a time transmission (TX), or more
  Synchronous/Asychronous
    Is there a clock signal, or not

## Slide 5: Bandwidth/Throughput
Max data TX rate
BW = Bus width (bits) x Frequency (Hz)/8 bits/byte
BW = 16bits x 66MHz = 132MBps

## Slide 6: Bandwidth
Be aware
  MBps = Megabytes per second
  Mbps = Megabits per second
    1 MBps = 8Mbps

## Slide 7: Bandwidth
Measurements made on decimal values
  1 MB = 1,000,000 bytes instead of 1,048,576 bytes
  Now 200 ‘MBps’ = 190 actual MBps
  Same reason why your ‘1TB’ SSD has 931GB in it

## Slide 8: Handshaking
Basic flow control – makes sure data is received or acknowledged

## Slide 9: Single Ended vs Differential
Cheaper
More noise immunity

## Slide 10: Buses
Picking a bus type will define many of these parameters

## Slide 11: Parallel Buses - PCI
1992-2003
Half-duplex
Synchronous

## Slide 12: Parallel Buses - PCIe
Multiple smaller parallel buses
Full-duplex, synchronous

## Slide 13: Parallel Buses - SCSI
Since 1981
Full-duplex, synchronous
Still popular for HD connections
  Now serial and parallel options

## Slide 14: Serial Buses – RS232
Or RS422/423/485
Asynchronous
Half or full-duplex

## Slide 15: Serial Buses - SPI
Since 1979
Full duplex, synchronous
Select line for each device
Wonderfully simple

## Slide 16: Serial Buses –I2C
Since 1982
Half-duplex, synchronous
Addresses

## Slide 17: Serial Buses - CAN
Very robust – auto applications
Differential
Asynchronous
Half-duplex

## Slide 18: Serial Buses - USB
Since 1982
Full-duplex (3.0), asynchronous
Addresses, packets,
and types

## Slide 19: Reading
This lecture
  Sections 13.6-13.9
Final Exam
  Friday May 6th, 9:50-11:50am